## Slide 1
DETECTION AND MITIGATION OF NDP ATTACK FOR AMI DEVICES IN SMART GRID
Presented by :
Purbasha Chowdhury
Sona Shaw
Premansu Kar
Guided under :
Dr.Nabendu Chaki

## Slide 2
In The Presentation
Introduction
India’s Electricity needs
What and why Smart Grid
Comparison
Smart Meter
AMI
IPV6 in Smart Grid System
Attack Scenario
Proposed Mitigation
Conclusion
25
2 of

## Slide 3
Introduction
India’s current Electricity Distribution scheme
Electric Power and Power Transmission
Present one-way Electric Transmission System
New idea to do more with less
Requirement of more devices
Environment and Technology
Reliable and Automated
Security and Threats
25
3 of

## Slide 4
Our Team Style
India’s Electrical Needs
(installed power capacity as on 31 Dec 2019)
25
4 of
Source: Mercom India Reasearch / powermin.nic.in
Electricity Generated

## Slide 5
WHAT IS SMART GRID?
• It is an electric grid that uses information and communication technology to gather data and act on information about the behaviour ofsuppliersand consumers in an automated fashion.
• Smart Grid is a generic label for the application of computer, intelligence and networking abilities to the existing dumb electricity distribution systems.
Why Smart Grid?
  Improve distribution management
  Self-sufficient & self-healing too
  Automation technology
  Sensing & measurement technologies
  Increased efficiency
  Sustainable & quality electricity
  Dynamic pricing mechanism
  Web portal & mobile apps
25
5 of

## Slide 6
Comparison
Electromechanical
Digital
One way transmission
Two way transmission
Centralized Organization
Distributed Organisation
Manual Monitoring
Self Monitoring
Not Reliable
Reliable
Conventional Grid
Smart Grid
25
6 of

## Slide 7
Our Team Style
Smart Meter
Smart Meter
What is Smart Meter
  Provides advanced functionalities of remote meter reading for collecting smart meter data
  Two way technology that can help to increase the reliability
  Recognizes and details electric consumption
  Power outrage notification & power quality monitoring
  Charges times of each day
Risks
Communicates via wireless network. So, possibility of hacking is high.
Once connected to the AMI which provides an access point for hackers. From there, hackers can adjust bills and take payment information.
The communication can be established via spoofed IP-MAC paired message came from an attacker to the genuine one.
25
7 of

## Slide 8
Our Team Style
Home Area Network (HAN)
Building Area Network (BAN)
Neighborhood Area Network (NAN)
Wide Area Network (WAN)
Classification of Smart Meter Network
Advance Meter Infrastructure
25
8 of

## Slide 9
1.
Compatible with the size of Smart Grid Network.
Need of IPV6 in Smart Grid System
2.
Large address space.
3.
Auto configuration of addresses.
4.
Efficient routing.
5.
Support prioritization of messages
IPv4
It can be configured manually
Fragmentation
IPSec is optional
Header includes a checksum
IPv6
Doesn’t require manual configuration
Without fragmentation
IPSec is mendatory
Header doesn’t include a checksum
25
9 of

## Slide 10
ICMPv6 attacks
ICMPv6 attacks
ICMP sweep
Inverse Mapping
ICMP Route Redirect
ICMP Route Discovery Message attack
Unique ICMPv6 attacks
Man In The Middle attack (MITM)
Duplicate Address Detection (DAD)
Neighbor Discovery Protocol (NDP)
25
10 of

## Slide 11
Our Team Style
ICMPv6 NDP Protocol
Router Solicitation (RS) message
Router Advertisement (RA) message
Neighbor Solicitation (NS) message
Neighbor Advertisement (NA) message
Router Redirect (RR) message
1
2
3
4
5
NDP uses five ICMPv6 messages
25
11 of

## Slide 12
Our Team Style
Smart Meter Communication
Smart meter – DCU (Data Collection Unit) connection
Connection Established
RS
IP(A)-MAC(A)
RA
IP(B)-MAC(B)
SM A
DCU B
Smart meter – Smart meter connection
SM B
NS
IP(A)-MAC(A)
NA
IP(B)-MAC(B)
Smart meter – DCU connection with RR
RR
IP(B)-MAC(B)
RS
IP(A)-MAC(A)
RA
IP(B)-MAC(B)
25
12 of

## Slide 13
Attack Scenarios
1. Spoofed RS message : Adversary SM wants to make connection with legitimate DCU.
SM A
DCU D
SM B
RS
IP(A)-MAC(A)
Spoof it
Spoofed RS
IP(A)-MAC(B)
RA
IP(D)-MAC(D)
Connection Established between B and D
25
13 of

## Slide 14
Attack Scenarios
2. Spoofed RA message : Adversary DCU wants to make connection with legitimate SM.
SM A
DCU D
RS
IP(A)-MAC(A)
Spoof it
Spoofed RA
IP(D)-MAC(B)
RA
IP(D)-MAC(D)
Connection Established between A and B
DCU B
25
14 of

## Slide 15
Attack Scenarios
3. Spoofed NS message : Adversary SM wants to make connection with legitimate SM.
SM A
SM B
NS
IP(A)-MAC(A)
Spoof it
Spoofed NS
IP(A)-MAC(B)
NA
IP(D)-MAC(D)
Connection Established between B and D
SM D
25
15 of

## Slide 16
Attack Scenarios
4. Spoofed NA message : Adversary SM wants to make connection with legitimate SM.
SM A
NS
IP(A)-MAC(A)
Spoof it
Spoofed NA
IP(D)-MAC(B)
NA
IP(D)-MAC(D)
Connection Established between A and B
SM D
SM B
25
16 of

## Slide 17
Attack Scenarios
5. Spoofed RR message : Adversary DCU wants to make connection with legitimate SM.
SM A
DCU D
RS
IP(A)-MAC(A)
Spoof it
Spoofed RR
IP(D)-MAC(B)
RR
IP(D)-MAC(D)
Connection Established between A and B
DCU B
DCU E
RA
IP(B)-MAC(B)
Connected
25
17 of

## Slide 18
Mitigation 1
The flow of messages is as packet format. Every packet has an unique IP address. Every corresponding neighbor has to keep track of the records to get rid of the spoofed attacks. Hence, there should be a cache of every neighbors in neighborhood.
DCU D
DCU C
SM B
SM A
Spoof it
RS
IP(A)-MAC(A)
Spoofed RS
IP(A)-MAC(B)
Extract SM’s address B=A
Echo Message
EchoReply = A
Check the majority decision of its neighbors.
Address didn’t matched and discard B’s RS
Spoofed RS
25
18 of

## Slide 19
Mitigation 1
DCU B
DCU A
SM D
SM C
Spoof it
RA
IP(A)-MAC(A)
Spoofed RA
IP(A)-MAC(B)
Extract SM’s address B=A
Echo Message
EchoReply = A
Check its own DCU address with its neighbor’s DCU address.
Address didn’t matched and discard B’s RA
Spoofed RA
RS
IP(C)-MAC(C)
25
19 of

## Slide 20
Mitigation 1
SM B
SM A
Spoof it
NS
IP(A)-MAC(A)
Spoofed NS
IP(A)-MAC(B)
Extract SM’s address B=A
Echo Message
EchoReply = A
Check the majority decision of its neighbors.
Address didn’t matched and discard B’s RS
SM D
SM C
Spoofed NS
NS
IP(A)-MAC(A)
25
20 of

## Slide 21
Mitigation 1
SM B
SM A
Spoof it
Spoofed NA
IP(D)-MAC(C)
Extract SM’s address D=C
Echo Message
EchoReply = D
Check the majority decision of its neighbors.
Address didn’t matched and discard C’s NA
SM D
SM C
Spoofed NA
NS
IP(B)-MAC(B)
NS
IP(A)-MAC(A)
NA
IP(D)-MAC(D)
NA
IP(D)-MAC(D)
25
21 of

## Slide 22
Mitigation 1
Spoof it
Spoofed RR
IP(A)-MAC(B)
Echo Message
EchoReply = A
discard B’s RR
SM D
SM C
Spoofed RR
RR
IP(A)-MAC(A)
RR
IP(A)-MAC(A)
DCU E
DCU B
DCU A
Connected
25
22 of

## Slide 23
Mitigation 2
Our proposed scheme ensures the genuineness of the IP-MAC pairing by an active verification mechanism. The scheme sends verification messages termed as NS/RS probe requests upon receiving RSs, NSs, RAs, NAs and RRs. Data tables for the proposed system are:
Router Solicitation Table(RST)
Router Advertisement Table(RAT)
Neighbor Solicitation Table(NST)
Neighbor Advertisement table (NAT)
Router Redirect Table(RRT)
Probe table (PRB)
Authenticated bindings table (AUTH)
Log table (LOG)
Unsolicited advertisement table (USAT)
We use the following short notations:
𝐼𝑃𝑆 - Source IP Address
𝐼𝑃𝐷 – Destination IP Address
𝑀𝐴𝐶𝑆 - Source MAC Address
𝑀𝐴𝐶𝐷 – Destination MAC Address
Fields of any table would be represented by ⟨𝑇𝑎𝑏𝑙𝑒𝑁𝑎𝑚𝑒⟩⟨𝑓𝑖𝑒𝑙𝑑⟩
⟨𝑇𝑎𝑏𝑙𝑒𝑁𝑎𝑚𝑒⟩𝑀𝐴𝑋 represents the maximum elements in the table at a given time
Mitigation for RS:
RS request is added to the Router Solicitation Table (RST).
RS packet is searched in Authenticate Binding Table (AUTH).
If (match) then status = GENUINE [IP-MAC pair is already recorded in AUTH table]
If (mismatch) then status = SPOOFED and spoofed packet details is recorded in LOG table.
If neither of the above cases occurred then the PROBE packet is sent to verify the genuineness of the packet.
Mitigation for RA:
Add RAPIPS, RAPMACS, RAPIPD and tau to the Advertisement table (RAT).
If ((RAPIPS = RSPIPD for some RSP present in the RST table) and (RAPIPS is found in AUTH table) and
(RAPMACS also matched))
Then
Status = GENUINE
3. Otherwise status = SPOOFED and spoofed packet detail is recorded in LOG table.
4. If the advertisement packet entry is not available in any Authenticated table, then a RS probe is sent to verify genuineness
Mitigation for NS:
NS request is added to the Neighbor Solicitation Table (NST).
NS packet is searched in Authenticate Binding Table (AUTH).
If (match) then status = GENUINE [IP-MAC pair is already recorded in AUTH table]
If (mismatch) then status = SPOOFED and spoofed packet details is recorded in LOG table.
If neither of the above cases occurred then the PROBE packet is sent to verify the genuineness of the packet.
Mitigation for NA:
1. Add NAPIPS, NAPMACS, NAPIPD and tau to the Advertisement table (NAT).
2. If ((NAPIPS = NSPIPD for some NSP present in the NST table) and (NAPIPS is found in AUTH table) and (NAPMACS also matched))
Then
Status = GENUINE
3. Otherwise status = SPOOFED and spoofed packet detail is recorded in LOG table.
4. If the advertisement packet entry is not available in any Authenticated table, then a NS probe is sent to verify genuineness.
Mitigation for RR:
RR request is added to the Router Redirect Table (RRT).
RR packet is searched in Authenticate Binding Table (AUTH).
If (match) then status = GENUINE [IP-MAC pair is already recorded in AUTH table]
If (mismatch) then status = SPOOFED and spoofed packet details is recorded in LOG table.
If neither of the above cases occurred then the PROBE packet is sent to verify the genuineness of the packet.
25
23 of

## Slide 24
Simulation
Trial Network
Our Approach:
Step 1: Create a NDP network between udp-server mote and udp-client mote and implement proposed attack scenario.
Step 2: Create a NDP network between udp-server mote and udp-client mote and implement proposed mitigation algorithm.
Step 3: Comparative study between step 1 and step 2.
Network creation between border-router and udp-sender motes
Terminal Window Output
Routing Table
Radio traffic between motes
Timeline Output
Mote Output
Simulation of Step 1
25
24 of

## Slide 25
  Conclusion
Smart grid technology utilizes the electricity maximum.
Smart grid reduces unnecessary wastages of electricity.
Smart grid helps to save the earth from global warming.
Here we proposed the respective attack scenarios based upon the five
NDP messages with respect to Smart Grid Environment and also the idea of the mitigation scheme of those attacks.
In the end of this presentation, we created the connection between server & client in perspective to smart meter communication in the simulation phase.
THANK YOU
25
25 of